Advanced Encryption Standard Cipher

Advanced Encryption Standard is a commonly used block cipher algorithm.
It uses 128 Bit input, called the “state” stored in a 4x4 matrix
The AES Algorithm Consists of four transformation steps called Sub Bytes, Shift Rows, Mix Columns and Add Round Key. Figure 1 shows a top level view of the Algorithm including the four steps. In the following paragraphs each of this steps will be explaind.

Sub Bytes:
Figure 1: AES Algorithm

Sub Bytes uses a substitution table (S-Box) consisting of several substitution values. In the Sub Bytes Step each byte of the state will be replaced with a byte from the S-Box. This provides a monalaphabetic encryption.

Shift Rows:
The rows of the state are left-shifted a specific
amount of bytes:
1. Row: none,
2. Row: 1 byte ,
3. Row: 2 bytes,
4. Row: 3 bytes

Mix Columns:
This step mixes the Data in the Rows via a multiplication of the bytes aj with a constant (either 1,2 or 3).

b_{0}=(a_{0} cdot 2) %UxE137 (a_{1} cdot 3) %UxE137 (a_{2} cdot 1) %UxE137 (a_{3} cdot 1)
b_{1}=(a_{0} cdot 1) %UxE137 (a_{1} cdot 2) %UxE137 (a_{2} cdot 3) %UxE137 (a_{3} cdot 1)
b_{2}=(a_{0} cdot 1) %UxE137 (a_{1} cdot 1) %UxE137 (a_{2} cdot 2) %UxE137 (a_{3} cdot 3)
b_{3}=(a_{0} cdot 3) %UxE137 (a_{1} cdot 1) %UxE137 (a_{2} cdot 1) %UxE137 (a_{3} cdot 2)

left[matrix{b_{0}##b_{1}##b_{2}##b_{3}}right] ~= ~left [matrix{2 # 3 # 1 # 1 ## 1 # 2 # 3 #1 ## 1 # 1 # 2 # 3 ## 3 # 1 # 1# 2} right ] ~left[matrix{a_{0}##a_{1}##a_{2}##a_{3}} right]

Add Round Key:
In the Initial Transformation and after each Round a so called KeyAddition takes place. This is the only step that depends on the Cipher Key.
It generates a new Round key for every Round from the old Round Key